## Slide 1: Cache Side Channel Attacks on Modern Processors
Yanan Guo
University of Pittsburgh
https://yananguo.com

## Slide 2: Outline
Background
Cache Attack -- Flush+Reload
Cache Attack -- Prime+Probe
Our work: Coherence-based cache attacks (S&P’22)
Defenses
Conclusion

## Slide 3: Side-Channel Attacks
Bug-free software does not mean safe execution.
Information may leak due to underlying hardware.
Exploit leakage through side-effects.
Power consumption
Execution time
Resource usage

## Slide 4
Cache timing side channel attacks:
Attacker monitors the victim's cache access utilization using timing information.

## Slide 5: Background: CPU Cache
DRAM
CPU
Slow!

## Slide 6: Background: CPU Cache
DRAM
CPU cache
Slow!

## Slide 7: Background: CPU Cache
printf("%d", a);
printf("%d", a);
Cache miss
Request
Response
DRAM
Slow!

## Slide 8: Background: CPU Cache
a
printf("%d", a);
printf("%d", a);
Cache miss
Request
Response
DRAM
Slow!

## Slide 9: Background: CPU Cache
a
printf("%d", a);
printf("%d", a);
Cache miss
Request
Response
Cache hit
Cache hit: faster, less than 60 CPU cycles.​
Cache miss: slower, over 200 CPU cycles.
DRAM
Slow!

## Slide 10: Background: CPU Cache
Cache line

## Slide 11: Background: CPU Cache
Set-associative cache
Memory Addresses
Set 0
Set 1
Set 2n
…
Way 0
Way 1
Way 2
Way 3
4-Way Associative Cache

## Slide 12: Background: Cache Attacks
Attacker and victim
  different processes
  Running on the same platform (usually different CPU cores)
Typical three steps:
  Step 1: Attacker evicts the data from a cache level.
  Step 2: Attacker waits for victim’s execution
  Step 3: Attacker checks whether the state of the data is changed
Repeating these three steps, attacker learns victim’s access pattern

## Slide 13
An example attack: Flush+Reload

## Slide 14: Flush+Reload
Attacker's goal:
  Learn the victim's access pattern on Line 0.
Assumption:
  Line 0 is shared between attacker and victim (e.g., shared library).
The cache line attacker is interested in.

## Slide 15: Flush+Reload
Step 1: The attacker flushes the victim’s data.
clflush:
An x86 instruction.
Takes a virtual address, flushes this address (cache line) from all cache levels.

## Slide 16: Flush+Reload
Step 1: The attacker flushes the victim’s data.

## Slide 17: Flush+Reload
Step 2: The attacker waits for the victim's execution.

## Slide 18: Flush+Reload
Step 3: The attacker reloads the data and times the reload operation.

## Slide 19: Flush+Reload
Step 3: The attacker reloads the data and times the reload operation.

## Slide 20: Flush+Reload
Victim
Attacker
Time
Access
Flush
Reload
Wait

## Slide 21
What can we leak?

## Slide 22: Attack 1: RSA Decryption Key
Input: base b, modulo m, exponent e = (en1...e0)2
Output: be mod m
r = 1
for i = n-1 down to 0 do
r = sqr(r)
…
if ei == 1 then
r = mul(r, b)
…
end
end
Spy addresses (instructions)

## Slide 23: Attack 2: Keystroke Logger
When a key is pressed, certain functions are called in the GDK library.
The attacker can monitor the accesses to that function to detect keystrokes.
How to find that function (addr)?
  Profiling...

## Slide 24
Another attack: Prime+Probe

## Slide 25: Prime+Probe
V
Set 0
Set 1
Set n
…
Way 0
Way 1
Way 2
Way 3
Step 1: Attacker evicts the victim’s data by priming the set.

## Slide 26: Prime+Probe
V
Set 0
Set 1
Set n
…
Way 0
Way 1
Way 2
Way 3
A1
Step 1: Attacker evicts the victim’s data by priming the set.

## Slide 27: Prime+Probe
V
Set 0
Set 1
Set n
…
Way 0
Way 1
Way 2
Way 3
A1
A2
Step 1: Attacker evicts the victim’s data by priming the set.

## Slide 28: Prime+Probe
V
Set 0
Set 1
Set n
…
Way 0
Way 1
Way 2
Way 3
A1
A3
A2
Step 1: Attacker evicts the victim’s data by priming the set.

## Slide 29: Prime+Probe
A4
Set 0
Set 1
Set n
…
Way 0
Way 1
Way 2
Way 3
A1
A3
A2
Step 1: Attacker evicts the victim’s data by priming the set.

## Slide 30: Prime+Probe
A4
Set 0
Set 1
Set n
…
Way 0
Way 1
Way 2
Way 3
A1
A3
A2
Step 2: Attacker waits for the victim's execution.

## Slide 31: Prime+Probe
A4
Set 0
Set 1
Set n
…
Way 0
Way 1
Way 2
Way 3
V
A3
A2
Step 2: Attacker waits for the victim's execution.

## Slide 32: Prime+Probe
A4
Set 0
Set 1
Set n
…
Way 0
Way 1
Way 2
Way 3
V
A3
A2
Step 3: Attacker accesses A1-A4 again and times the access.

## Slide 33: Cache Attack
Stateful Cache
Attacks
Conflict-Based Attacks
Eviction
Method
Prime+Probe (2005),
Evict+Reload (2015), Evict+Time (2006), Prime+Abort (2017), Prime+Scope (2021), Evict+Prefetch (2016)…
Flush-Based Attacks
Flush+Reload (2013),
Flush+Flush (2015), Flush+Coherence (2018), Invalidate+Transfer (2015), Reload+Refresh (2020)…
Can we find new attack methods?

## Slide 34: Cache Attack
Stateful Cache
Attacks
Flush-Based Attacks
Conflict-Based Attacks
Eviction
Method
Can we find new attack methods?
Flush+Reload (2013),
Flush+Flush (2015), Flush+Coherence (2018), Invalidate+Transfer (2015), Reload+Refresh (2020)…
Prime+Probe (2006),
Evict+Reload (2015), Evict+Time (2006), Prime+Abort (2017), Prime+Scope (2021), Evict+Prefetch (2016)…
???

## Slide 35: Our Work (S&P 2022)
Stateful Cache
Attacks
Flush-Based Attacks
Conflict-Based Attacks
Eviction
Method
Can we find new attack methods?
Flush+Reload (2013),
Flush+Flush (2015), Flush+Coherence (2018), Invalidate+Transfer (2015), Reload+Refresh (2020)…
Prime+Probe (2006),
Evict+Reload (2015), Evict+Time (2006), Prime+Abort (2017), Prime+Scope (2021), Evict+Prefetch (2016)…
Coherence-Based Attacks

## Slide 36: Cache Coherence
Data can be shared by processes/cores.
How do know a copy of cache line is readable/writable?
  Need to track the coherence state of each copy of a cache line.

## Slide 37: Cache Coherence
x86 processors use MESI (or the variants).
    With MESI, invalidation happens upon writes.
Require for ownership (RFO)

## Slide 38: Key Insights
Cache coherence protocol can be used for eviction.
  RFO can cause cross-core private cache invalidation.
  It only happens upon writes.
  The shared data between the attacker and victim is typically read-only.
  Attacker needs to cause RFO without writing the cache line.
  Against the design principle, but maybe possible due to implementation flaws.

## Slide 39: Key Insights
x86 data prefetching instructions
  PREFETCHT0, PREFETCHT1, PREFETCHT2 …, for reads.
  PREFETCHW, for writes.
PREFETCHW
  It prefetches the data into the private cache and changes the coherence state to Modified.
  On Intel Core i7-6700, Core i7-6800K, Core i7-7700K, Core i9-10900X,
    Property 1: PREFETCHW works on read-only data.
    Property 2: PREFETCHW has timing variance.
  PREFETCHW is available since Broadwell.
    Are the two properties always true on Intel processors?

## Slide 40
Processor | Microarch. | LLC Type | Property #1 | Property #2
Core i7-6700 | Skylake | Inclusive | Yes | Yes
Core i7-6800K | Skylake | Inclusive | Yes | Yes
Core i7-7700K | Kaby Lake | Inclusive | Yes | Yes
Core i9-10900X | Cascade Lake | Non-inclu. | Yes | Yes
Xeon Silver 4114 | Skylake-SP | Non-inclu. | Yes | Yes
Xeon Plat. 8151 | Skylake-SP | Non-inclu. | Yes | Yes
Xeon Plat. 8124M | Skylake-SP | Non-inclu. | Yes | Yes
Xeon Plat. 8175M | Skylake-SP | Non-inclu. | Yes | Yes
Xeon Plat. 8259CL | Skylake-SP | Non-inclu. | Yes | Yes
Xeon Plat. 8275CL | Skylake-SP | Non-inclu. | Yes | Yes
Xeon Plat. 8375C | Ice Lake | Non-inclu. | Yes | No
Key Insights

## Slide 41: Our proposal
Two cross-core private cache attacks
  Prefetch+Prefetch
  Prefetch+Reload
Threat Model
  Attacker and victim are on different processor cores.
  Attacker can share data with the victim (e.g., through shared library).
  In Prefetch+Prefetch, the attacker has (at least) one thread.
  In Prefetch+Reload, the attacker has (at least) two threads.

## Slide 42
Prefetch+Prefetch

## Slide 43
Can we load and time the load instead?
Not by the same attacker’s thread.
Prefetch+Prefetch

## Slide 44
Prefetch+Prefetch
Can we load and time the load instead?
Not by the same attacker’s thread.
What if the attacker has a second thread?

## Slide 45
Prefetch+Reload

## Slide 46
Prefetch+Reload

## Slide 47
Evaluation-Side Channel
Input: base b, modulo m,
exponent e = (en1...e0)2
Output: be mod m
r = 1
for i = n-1 down to 0 do
r = sqr(r)
…
if ei == 1 then
r = mul(r, b)
…
end
end
Prefetch+Prefetch Result

## Slide 48
Evaluation-Side Channel
Prefetch+Reload Result

## Slide 49
Evaluation-Side Channel
Compared to Flush+Reload?
  Much higher temporal resolution.
Flush+Reload requires a waiting window
  The window needs to be long enough to not miss a victim's event.
  But Prefetch+Prefetch does not need a waiting window.
  Temporal resolution: ~100 cycles VS 4000 cycles
Wait

## Slide 50: Evaluation-Covert Channel
Covert Channel (隐蔽信道)
Processor | Prefetch+Reload | Prefetch+Load | Prefetch+Prefetch
Core i7-6700 | 631 KB/s | 709 KB/s | 721 KB/s
Core i7-7700K | 782 KB/s | 840 KB/s | 822 KB/s
Xeon Plat. 8124M | 394 KB/s | 586 KB/s | 556 KB/s
Xeon Plat. 8151 | 476 KB/s | 680 KB/s | 605 KB/s
Flush+Reload: ~270 KB/s

## Slide 51: Evaluation-Covert Channel
With transient execution attacks
  1) The covert channel speed determines the leakage rate of transient execution attacks
    Spectre v1 with Prefetch+Prefetch vs Spectre v1 with Flush+Reload: 3.02* faster
    Spectre v1 with Prefetch+Reload vs Spectre v1 with Flush+Reload: 1.61* faster
  2) Prefetch-based covert channels: faster encoding operation
    More secret bytes can be leaked within the transient window
    In the Spectre-V1 window
      8 bytes can be leaked with Flush+Reload
      17 bytes can be leaked with Prefetch+Prefetch
If (x+n < array1_size){
y0 = array2[0][array1[x] * 4096];
y0 = array2[0][array1[x] * 4096];
…
y0 = array2[0][array1[x] * 4096];}
If (x< array1_size)
y0 = array2[array1[x] * 4096];

## Slide 52: Defense
How to defend prefetch-based attacks?
  Add permission check on prefetchw
  Avoid data sharing among processes
    Will waste a lot of memory
  Modify the cache coherence protocol
    Chenlu Miao et al. "SwiftDir Secure Cache Coherence Without Overprotection". In MICRO 2022.

## Slide 53
Thanks!